Class 1 Operator Knowledge EXAM

What is the most common type of lift truck accident?

a. Fallen load

b. Truck tipped over

c. Pedestrian hit by a lift truck

d. Worker hitching a ride fell off the truck

If you have been trained to operate a sit-down four-wheel lift truck, you are also qualified to operate a stand-up reach truck.

a. True

b. False

When is completion of the pre-operation inspection checklist necessary?

a. Once a month

b. Once a week

c. Daily

d. At the beginning of every shift

e. c and d

Only trained and authorized operators are allowed to operate a forklift.

a. True

b. False

Is it OK to operate a lift truck that does not have a Data plate or the Data plate is damaged or unreadable?

a. Yes

b. No

When traveling with a load on a level surface, you should raise the forks approximately how high from the floor?

a. 4-6 inches

b. 2-3 feet

c. Eyelevel with the operator

d. None of the above

Loads should always be carried with the mast tilted to the forward-most position.

a. True

b. False

When is it ok to give someone a ride on the lift truck?

a. Never

b. As long as they remain under the overhead guard

c. If the supervisor says it's OK

d. Only when driving very slowly

The rear-end steering of a fork lift:

a. Is similar to an automobile

b. Causes the rear end swing to the outside of the turn

c. Causes the front end swing to the out about the same as a car

d. Allows the forklift to make sharp turns at high speed

When depositing a load, lower the forks until there is slack in the chains before backing out.

a. True

b. False

For which of the following is lift truck operator safety training most important?

a. Lift trucks last longer

b. Helps prevent accidents

c. Makes more profits

d. Drivers are more efficient

All lift trucks have the same controls and gauges.

a. True

b. False

Is a fork truck considered in good operating condition even if the some of the gauges are broken?

a. Yes

b. No

The person charging or replacing the battery of an electric lift truck should always wear:

a. Protective gloves with gauntlets

b. Eye or face protection

c. An apron resistant to battery acid

d. All of the above

If you know how to drive a car, you also know how drive a lift truck.

a. True

b. False

What should be done if a lift truck is found to be in need of repair, defective or in any way unsafe to operate.

a. Operate the lift truck anyway and inform supervisor at the end of the shift

b. Inform supervisor immediately and red-tag or take out of service.

c. Make repairs yourself

d. Inform maintenance and then operate as usual

What should the operator do before driving a lift truck into a trailer?

a. Make sure the trailer is able to handle the additional weight of the lift truck

b. Check that the tire blocks are securely in place in front of and behind the trailer tires

c. Check that the jack stands for the trailer are in place

d. Inspect dock leveler or dock plate

e. All of the above

When traveling up or down a grade or ramp, the load should always point uphill.

a. True

b. False

Who is responsible for preventing accidents in the workplace?

a. Truck operator

b. Everyone

c. Supervisor

d. Safety inspector

Which of the following items will take your lift truck out of service?

a. Leaking hydraulics hoses

b. Faulty brakes

c. Steering problem

d. Parking brake will not engage

e. All of the above

Railroad tracks should always be crossed straight on and not at an angle.

a. True

b. False

If a load appears to be improperly stacked or unstable:

a. Lift the load carefully and drive slowly

b. Straighten the load so it is safe to move

c. Drive in reverse so the load does not fall on you

d. None of the above

It is OK to do a quick battery charge during a lunch break on an electric lift truck.

a. Yes

b. No

When refueling a gas or diesel lift truck:

a. Place your cigarette away from the truck

b. Leave the engine running

c. Raise the forks 4 to 6 inches off the floor

d. Fill tank until there is a slight overflow

e. None of the above

Lift trucks are designed so that the center of gravity remains the same loaded or unloaded.

a. True

b. False

If a lift truck begins to tip over sideways, the operator should

a. Release the seat belt and jump away from the direction the truck is tipping

b. Stay in the truck and ride it out

c. Set the parking brake and sound the horn

d. None of the above

Before changing an LP bottle, the service valve must be shut off and the engine left running until it stops.

a. True

b. False

It's OK to operate the lift truck when the following is missing or damaged:

a. Manufacturers safety warning decals

b. Mast chains are out of adjustment

c. No seat belt is present or does not operate properly

d. Parking brake does not engage fully

e. None of the above

Pedestrians should always yield right-of-way to a lift truck.

a. True

b. False

# Text boxes

Forklift Class 1
Operator Knowledge EXAM

.
.
.
.
.
.
.
.
.